int ledA = 7;
int ledB = 6;
int count=0;
void setup()
{
  Serial.begin(9600);
}

void loop()
{
  Serial.println("LED as touch sensor");
  pinMode(ledA, OUTPUT);
  pinMode(ledB, OUTPUT);
  //Discharge the capacitance on the LEDS
  digitalWrite(ledA, HIGH);
  digitalWrite(ledB, LOW);
  
  delay(1);
  //Charge the capacitance on the LEDs
  digitalWrite(ledA, LOW);
  digitalWrite(ledB, HIGH);
  
  delay(1);
  pinMode(ledB, INPUT);
  //Wait for LED to become low
  
  while(digitalRead(ledB))
  count++;
  
  Serial.println(count);
  
  count =0;
  
  delay(2000);
}